## Slide 1: Real satellite telemetry through our autonomous receiver
Track 1 · Part 3 · 861 real SatNOGS frames, one hostile channel, zero human tuning
Notes: This section tests whether REAL satellite telemetry survives our simulated deep-space link. Every byte is checked against the original.

## Slide 2: 861 real frames from 27 ground stations
861
telemetry frames
27
ground stations
138
observations
1 week
Sept 26 to Oct 3, 2026
What a frame looks like
hex 47 32 20 30 30 30 20 30 4E ...
text G2 000 0N I TE25 000 TEOT
hex 33 34 39 39 34 39 32 30 30 ...
text 3499492000005025000000
CW (Morse) beacon frames decoded to text by SatNOGS stations. Original reception errors are kept as-is.
Notes: Source: SatNOGS DB, one week of frames for one satellite (add its name). The cleanest beacon string, 3499492000005025000000, appears 21 times; the garbled ones are noisy copies from the stations' Morse decoders.

## Slide 3: Real telemetry through a hostile channel
1
Real frames
861 SatNOGS frames, 9 to 63 bytes
2
Frame them
Add sync word, sequence, length and a CRC
3
Hostile channel
Doppler drift, dropout, frequency hop, noise
4
Autonomous receiver
Track, re-acquire, classify (IQNet), demodulate
5
Verify
Check the CRC, then compare every byte
The receiver is never told the modulation, the frequency, or when the signal drops out.
Notes: Script: satnogs_frames.py. Step 2 mimics a spacecraft radio (CCSDS sync word 0x1ACFFC1D). Step 4 reuses pipeline.py: squaring/4th-power carrier tracking, re-acquisition with hysteresis, IQNet classification, differential demodulation.

## Slide 4: The receiver straightens a drifting signal
Before: Doppler curve, dropout at 8.7 s, hop at 14.4 s. After: a steady signal at 0 Hz for the whole pass.
Notes: Required Track 1 output: before/after spectral plot. Left = raw received signal carrying the real frames. Right = after autonomous carrier tracking, mixdown and matched filtering.

## Slide 5: 99% of real frames survive from 0 dB up
Chart: Byte-exact recovery vs SNR (dB per sample)
| -6 | -4 | -2 | 0 | 2 | 4 | 6 | 8
Frames recovered (%) | 0 | 9 | 66 | 98 | 99 | 99 | 99 | 99
99.2%
854 of 861 frames recovered byte-exact at 2 dB
95%
IQNet confidence the signal is BPSK, with no human input
Notes: Classic digital-link cliff: almost nothing below -4 dB, steep climb, flat near 99% from 0 dB. It tops out just under 100% because frames sent during the dropout cannot be recovered by any receiver.

## Slide 6: Losses line up with channel events
0.0 s
Acquired
Carrier found at +1509 Hz
8.7 s
Dropout
Frames 261 to 264 lost, re-acquired 0.13 s later
14.4 s
Hop
Frames 438 to 439 lost, re-acquired at once
28.8 s
Classified
IQNet: BPSK, 95% confident
The single other loss (frame 772) is random noise, expected now and then at 2 dB.
Notes: Green = recovered byte-exact, red = lost. Times come from events.log. This shows the autonomy: the receiver notices each problem and recovers on its own.

## Slide 7
What this shows, and what's next
Shows
Real telemetry is delivered byte-for-byte through drift, dropouts and hops
Fully autonomous: no tuning, no modulation hint
A RadioML-trained CNN works inside the live receiver
Limits and next steps
Channel is simulated, not real RF
Frames are CW text: we test delivery, not this satellite's field decoding
Next: real BPSK recordings and satellite-specific decoders
Notes: Close by linking back to the full pipeline: this part proves the decoded output is trustworthy; the observation part (friend) shows the front end on real radio signals.